## Slide 1: Module 3 SARS-CoV-2 whole genome sequencing
Sequencing using NextSeq 550
Date : 19 May 2021
Dr Arshad Ismail
Zama Khumalo
Thabo Mohale
National Institute for Communicable Diseases, South Africa

## Slide 2: Sequencing Workflow
Sequencing
Step 1
Step 2
Washing of the Machine
Loading of Libraries
Run - QC Metrics
Create Sample Sheet
Step 3
Step 4

## Slide 3
NextSeq 550
Run Time | 12–30 hrs
Maximum output | 120 Gb
Maximum Reads per Run | 400 million
Maximum Read Length | 2 × 150 bp
Specifications

## Slide 4: Sequencing Kit Components
1. Buffer Cartridge
1
2. Loading Cartridge
2
3
3. Flow cell

## Slide 5: STEP 1
Washing of the Machine
Quick Wash
  Quick wash is performed before every sequencing Run
  A wash solution of 40 ml of laboratory-grade water mixed with 20 µl Tween 20 (0.05% Tween 20 final concentration)
  Wash takes about 20 minutes

## Slide 6: STEP 2
Sample Sheet
Loading a sample sheet onto the NextSeq 550

## Slide 7: STEP 3
Cleaning & inspecting of the Flow Cell
Loading Flow cell in the compartment
Illumina NextSeq Control Software
Loading of Buffer Cartridge

## Slide 8: STEP 4
Loading of Libraries
Loading Libraries into Reagent Cartridge
Pierce foil with a new pipette on the well-marked “Load Libraries Here”
Add libraries (650 µl x2 ) to the bottom of the well
Gentle tap the cartridge
Slide the reagent cartridge into the reagent compartment until the cartridge stops,
Close the reagent compartment door

## Slide 9
NextSeq 550 system check

## Slide 10: Run QC Metrics

## Slide 11: Data analysis
This concludes the wetlab portion of the Illumina CovidSeq workflow
In the next session - in silico part of DNA sequencing, where softwares are used to assemble and analyze the raw data output of the next-generation sequencers